Rev D
Plug	Description	ESP32 I/O	Wire spec
Black plug	12 volt system
1	12V steer enable switch	15	18GA Orange
2	CAN LO	32 ?	18GA Green
3	CAN HI	33 ?	18GA Yellow
4	Steer motor / valve PWM	25	18GA White
5	Steer motor / valve PWM	26	18GA Gray
6	Steer motor / valve PWM Danfoss	27	18GA Brown
7	Safety alarm	4	18GA
8	12V work enable switch	5	18GA Pink
9	GND		14GA Black
10	GND		14GA Black
11	12V+ control logic input (ESP32)		18GA Purple
12	12V+ steer motor / valve input		14GA Red

Gray plug	5 volt system
1	GND		18GA Black
2	GND		18GA Black
3	Steering wheel encoder	23	18GA Blue
4	Wheel Angle Sensor (WAS) feedback	ADS1115 A0 Single	18GA GR/WH
5 (4+5)	Wheel Angle Sensor (WAS) feedback	ADS1115 A0 Differential	18GA YL/WH
6	5V+ for sensor		18GA Red
7	5V+ for sensor		18GA Red
8	5V work enable switch	5	18GA BL/WH
9	5V steer enable switch	15	18GA WH/RED
10
11
12

Led Pinout

Led	ESP32 I/O
Work led	14
Steer led	12
WiFi led	13

Steer and work switch inputs
The 5 volt steer (or work) enable and the 12 volt steer (or work) enable are hooked together internally using different value resistors and both end up at the same ESP32 GPIO.

Steering motor / valve outputs
The steer motor/valve output is compatible with hydraulic valves, but not steering motors, since it lacks low side drivers. Output pin 4&5 are capable of driving high side only. Output pin 6 is capable of driving high and low side, and has balanced rising and falling edges, good for Danfoss valves.

Pin 4&5 are 3 amps max. Pin 6 is 1/2 amp (500mA) max.

Steering wheel encoder input
The steering wheel encoder input is sourcing, meaning it needs a negative signal. Positive inputs will not trigger. Note that this is for a switch or encoder on the steering wheel shaft to detect rotation, not any buttons that may exist on the steering wheel for other functions.

5 volt plug
500mA max supply
Do not connect GND terminals to machine GND. Use GND terminals for sensor or switch supply.

Diagnostic LEDs
Str Sw lights up if the steer enable switch is pressed.
Wrk Sw lights up if the work enable switch is pressed.
Str Whl Sw blinks as the steer wheel is turned.
Power will light up when the 12V logic supply is on. This does not mean the ESP32 is working.
Wifi will show if the ESP32 successfully connected to a network.
Steer and Work show the status of the commands from AOG.

Wheel Angle Sensor (WAS)
If your WAS is the newer style with opposing dual feedback, try the differential mode for greater accuracy, and for zero counts when the wheels are straight ahead.